| RELAY | RELAY NUMBER | RELAY DESCRIPTION |
| --- | --- | --- |
| A | 3.13 | Headlight |
| B | 3.04 | Terminal 75 |
| C | 3.03 | Ignition (Terminal 15) |
| D | 3.22/3.16 | Relay, Auxiliary Water Pump (B18EP/FP engines)/Relay, Auxiliary Water Pump (B18FT engine) |
| E | 3.05 | Air Conditioning |
| F | 3.06 | Double Acting-Headlight Motors |
| G | 3.14 | Inhibitor, Headlight Dim-Dip System |
| H | 3.08 | NOT SHOWN IN HAYNES MANUAL (Possibly Fog light?) |
| J | 3.10 | ABS Power |
| K | 3.09 | ABS Pump |
| L | 3.11 | Bulb Failure Detector, Front Bulbs |

| FUSE | DESCRIPTION | AMP |
| --- | --- | --- |
| 1 | Blower Speed 1,2,3,4 |  |
| 2 | Radio Search Light Radio RHD |  |
| 3 |  |  |
| 4 | Mirro 2x |  |
| 5 |  |  |
| 6 | Wiper & Washer Motor Front & Rear Heated Seats |  |
| 7 | Airco Compr Brake Lights Spd 1 Electric Fan |  |
| 8 | Central Door Lock Long Range Lights Horns |  |
| 9 | Wiper Motor Front & Rear Via CEM |  |
| 10 | Hazard Warning & Direct Light Washer Head Lamp |  |
| 11 | Rear Fog Lamp LHD |  |
| 12 | Fuel Pump |  |
| 13 | Heated Lambda Sonde |  |
| 14 | Dipped Beam Left |  |
| 15 | Dipped Beam Right |  |
| 16 | Supply Instrument |  |
| 17 | Panel Instrument Illuminated Light Switch CEM |  |
| 18 | Reverse Lights Heating Airco Rear Bulb Failure |  |
| 19 | Day Running Lights Dip Dim RHD |  |
| 20 |  |  |
| 21 | Supply Cigar Lighter Instrum Radio Illum Lock | 10 |
| 22 | Illum Glove Box Luggage Interior Clock |  |
| 23 |  |  |
| 24 | Light Flash Front Fog Light Rear & Front |  |
| 25 | Rear De-Mist Heated Mirror 2x |  |
| 26 | Pop Up Motor L&R |  |
| 27 | Window Lifts MoonRoof |  |
| 28 | Parking Left & Rear Light L&R Rheostat Dip Dim |  |
| 29 | Parking Left & Rear Light L&R Fog Lights Rear & Front |  |
| 30 | Main Beam Left CEM |  |
| 31 | Main Beam Right Switch Long Range Dip Dim |  |
| 32 | ABS |  |

# Text boxes

1

2

3

4

5

6

7

8

9

10

11

12

13

14

15

16

17

18

19

20

21

22

23

24

25

26

27

28

29

30

31

32