Facts / Tips & tricks

Identified relays

The relaybox on my 1989 480ES (Sweden) from no. 529392. The relays are not described in the car-manual or Haynes repair-manual.
Attention, these relays change according to modeles, in particular from the models on 1994 (No. 581011)

Relay-box overview

1. Hella Lampcontrol 12V, Class 3, 448130, 5KG005918-01, Running lamp 2x21W

2. ABS Pump-relay

3. foglights (white for the Netherlands (3,08 Silver), for Europe (3,12) 

4. 412653 12V/20A, Popup-lights

5. Wehrle 59205001, Electrical water pump (EP/FP, red:3,16)or(FT, yellow:3,22)

6. ABS pump, electrical relay mark 2 (3,09 red)

7. Empty, What for? (antifogs rear (NEDERLAND 3,07)

8. Air conditioning for european cars (3,05), earlier antifogs for the Netherlands(3,12)

9. Pop-Up relay, 5DS0050053-00

10. Wehrle 20 210006, Ignition relay contact 15 (3,03)

11. Wehrle 20 210006, Fusebox relay contact 75 (3,04))

12. Contact for diagnosis ABS mark 2